RPCR.DOC     MVS Box850 Merrimack,NH     5/6/92

The Remote Power Card Reset version (RPCR) is a 1/4 slot card that
plugs into an XT/AT type computer.  This card reboots the computer
should it become locked up for hardware or software reasons.

The RPCR functions by maintaining a timer seperate from the computer. 
When this timer reaches terminal count it causes the same effect as
pressing the Reset button.  Reboot can be prevented by writing a 1 and
then a 0 to the Counter Clear Address.  This causes the count to begin
again.  The computer will only be reset if this routine does not run,
such as when the computer is locked up.

The card installs in one of the motherboard slots.  Since the PC Bus
has no polarizing keys it is very important that the component side of
the card be facing the same direction as the other adapter cards.

    *************************************************************
    *   WARNING !!!  THE RPCR MUST FACE THE SAME DIRECTION AS   *
    *      OTHER CARDS IN THE PC OR DAMAGE WILL RESULT !!!!     *
    *   PLUGGING THE RPCR IN BACKWARDS WILL VOID THE WARRANTY.  *
    *************************************************************

The only connection to the card other than the PC Bus is a thin wire
with a connector on the end.  This wire plugs onto one of the
motherboard pins that go to the Reset button.  You can either remove
the cable that goes to the Reset button or splice into it.  If the RPCR
does not function then try the other one in the pair.  The RPCR signal
is an open-collector transistor so relays, indicators, and other
devices can be activated instead of Reset if necessary.

Testing is simple.  With no special software running and the RPCR
installed the computer will reboot once every four minutes.  In each
cycle there is a two minute delay followed by Reset being activated for
two minutes more.  Most computers boot faster than the Reset Delay
period giving AUTOEXEC.BAT enough time to run the user program.  During
normal operation the user program clears the timer at intervals of less
than two minutes to keep from rebooting.

Reset remains asserted for two minutes.  This gives modems, phonelines,
printers and other peripherals time to settle into a known initial
state.  When released the computer starts booting immediately.

If necessary the Reset Delay time can be altered and the Counter Clear
Address may be changed via jumpers.  Reset Delay values are guaranteed
to be equal to or greater than indicated.  Remember to cut the default
run before adding new jumpers.

Reset Delay Jumpers:     Settings:            22-16 = 4 sec
  J9 10 11 12 13 14 15    J22-J14 = 1/16 sec  22-18 = 8 sec
   o  o  o  o  o  o  o      22-15 = 1/8 sec   22-12 = 16 sec
   o  o  o  o  o  o  o      22-21 = 1/4 sec   22-13 = 32 sec
 J16 17 18 19 20 21 22      22-20 = 1/2 sec   22-10 = 64 sec
                            22-19 = 1 sec     22-17 = 128 sec (default)
                            22-11 = 2 sec     22-9  = 256 sec
Counter Clear Address:
    J1 J2 J3 J4              121h = J1-J6 2-5 3-7 4-8
     o  o  o  o              181h =   1-5 2-6 3-7 4-8 (default)
     o  o  o  o              221h =   1-6 2-5 3-8 4-7
    J5 J6 J7 J8              281h =   1-5 2-6 3-8 4-7

Several demo programs are included showing how to use the RPCR with
Assembly, BASIC, and C.  These programs intentionally lock up the
computer when a key is pressed.  The RPCR will reboot it!

                      WARRANTY
MVS will repair free of charge boards suffering from manufacturing
defects for a period of 60 months after shipping.  This will be done
only if it has been determined by MVS that the product has not been
misused (improper supply voltages, physical alteration, etc.). 
Otherwise a minimum service charge is required.  In either case it is
necessary to contact the company for a Returned Merchandise
Authorization (RMA) number before shipping the unit.

MVS assumes no responsibility for damage or other loss resulting from
use of this product or modifications associated with it.

No part of the RPC circuit shall be duplicated in any way without
permission from MVS.  The design is protected under Civil and Criminal
Law.  Manufacturing licenses for products are available from MVS in
addition to significant OEM discounts.  Contact the company for more
information.