NAME
     prof - a program for profiling .COM & .EXE programs.

SYNOPSIS
     prof [ options ] cmd [ args ]

DESCRIPTION
     Prof is a program that collects information about where a
     program spends most of its time executing, and a few other
     things. It is not dependent of a specifiec compiler or
     language, but requires a standard mapfile to be any useful.
     Assembler programs work fine, but not with mixed near/far
     calls if you use the `-m' switch. The results of the profile
     are not affected by the time it takes to load the profiled
     program from disk.

OPTIONS
     -2   Assume near function calls; that is, the program to be
          profiled should have been compiled under the Tiny,
          Small or Compact memory models. Near function calls are
          assumed by default.
          This switch is meaningful only in combination with the
          `-m' switch.

     -4   Assume far function calls, i.e. Medium, Large or Huge
          memory models. Otherwise as for `-2'.

     -Ad  Set the sampling precision to d, where d is a digit
          between 1 and 9 inclusive. 1 means maximum precision,
          9 means minimum. If d is not specified, a precision of
          1 is set by default. If this switch is not specified
          at all, a sampling precision slightly worse than 9 is
          applied.
          Note that the sampling is not performed more *often*
          when a higher precision is used; the sampler is rather
          wasting more time in a delay loop (i.e. the clock freq-
          uency is not adjusted). The happy effect of this is
          that it works on the 8086/8088, the boring effect is
          that the profiled command might run *very* slowly.
          This switch is maningful only in combination with `-f'
          or `-l'.

     -Mx  Use mapfile `x' instead of the default name, which is
          diverged from the command name by appending ``map''.

     -a   Sort the output by address.

     -c   Count the number of calls to each function.

     -d   Count the number of calls to each DOS function
          (int 21h), and subfunctions where that is applicable.
          You won't get symbolic names, though. Does not require
          a mapfile.

     -f   Estimate the relative time spent in each function and
          DOS/BIOS areas. This is the default operation of the
          profiler. May produce strange output if there are a lot
          of static (or private) functions in the program. This
          applies certainly to the runtime library.
          Does not require a mapfile to report DOS/BIOS areas
          versus the code executed in the command itself.

     -i   Interactive turn profiling on and off by use of the
          key combinations Alt+ (on) and Alt- (off). Profiling
          is off at startup.

     -j   As `-i', but profiling is on at startup.

     -k   Count the number of times each line executes.

     -l   Estimate the relative time spent executing each line
          in the program. Every sample that doesn't match a line
          is labeled ``Runtime library'' in the output.

     -mx  Track down all calls to function `x' and report where
          they came from. This may *really* produce funny results
          if there are a lot of static functions. C programmers:
          remember to prepend the underscore!

     -n   Sort the output by name. Not applicable when profiling
          line numbers or counting DOS calls.

     -ox  Use output file `x' instead of the default name, which
          is diverged from the command name by appending ``prf''.

     -q   Sort the output by frequency. This is the default.

     -s   Swap the names collected from the mapfile to disk upon
          execution of the command. This to free up some core.

     -v   Verbose. Report memory usage and exit status of
          profiled command.

     -w   Some compilers produce strange line number information
          in the mapfile. This includes different line numbers
          with the same address, and the same line number/address
          pair repeated. In each of these cases the duplicate
          information is discarded. `-w' means to give a warning
          each time this happens.

     -z   List also items that had zero frequency. Not applicable
          to DOS calls.

     cmd  The command to be profiled, may be a .COM or an .EXE
          program. Full path name must be supplied.

     args Arguments to profiled command.

     The switches `-c', `-d', `-f', `-k', `-l' and `-m' are
     mutually exclusive, as are also `-a', `-n' and `-q'.

LIMITS
     The current version has a maximum limit of 5458 functions or
     lines. The line maximum is too restrictive, so this might be
     classified as a bug.

BUGS
     The results of the `-c' switch may vary slightly from run to
     run (they are too high), especially for functions that are
     called a lot of times. Why this happens is beyond my under-
     standing, but the variations are so small (0.01%) that the
     effect should be zero. The same appears for the `-k' switch.

     The profiler might hang when a high sampling precision is
     used. This *should* never happen, but anyway it does.

ACKNOWLEDGEMENTS
     This program is a major rewrite of Bjorn Larsson's profiler,
     which i downloaded from somewhere some day. The original
     version was only able to profile functions (`-f' switch).